## Slide 1: Enabling ECN in Multi-Service Multi-Queue Data Centers
Wei Bai, Li Chen, Kai Chen, Haitao Wu (Microsoft)
SING Group @ Hong Kong University of Science and Technology
Notes: Hello everyone, I am Wei Bai from Hong Kong University of Science and Technology. Today I am going to talk about our work, enabling ECN in multi-service multi-queue data centers. This is a joint work with Li Chen, Kai Chen from Hong Kong University of Science and Technology and Haitao Wu from Microsoft.

## Slide 2: Background
Data Centers
  Many services with diverse network requirements
Notes: The context of this work is data center. As we know, today’s data centers host many services and applications with diverse network requirements. Some services desire high throughput. Some services desire low latency. Some services desire both high throughput and low latency.

## Slide 3: Background
Data Centers
  Many services with diverse network requirements
ECN-based Transports
  ECN = Explicit Congestion Notification
Notes: To satisfy such diverse network requirements, many people have leveraged ECN, explicit congestion notification, to design new transport mechanisms for data center networks.

## Slide 4: Background
Data Centers
  Many services with diverse network requirements
ECN-based Transports
  Achieve high throughput & low latency
  Widely deployed: DCTCP, DCQCN, etc.
Notes: With ECN, we can achieve high throughput even with little buffer occupancy. Due to their simplicity and effectiveness, many ECN-based transports, such as DCTCP and DCQCN, are being deployed in production data centers.

## Slide 5: ECN-based Transports
Notes: ECN-based transports actually consist of two parts.

## Slide 6: ECN-based Transports
ECN-enabled end-hosts
  React to ECN by adjusting sending rates
Notes: The first part is ECN-enabled end-hosts. End-hosts reduce their sending rates when they see ECN marks.

## Slide 7: ECN-based Transports
ECN-enabled end-hosts
  React to ECN by adjusting sending rates
ECN-aware switches
  Perform ECN marking based on Active Queue Management (AQM) policies
Notes: The other part is ECN-aware switches. Switches need to perform ECN marking based on AQM policies to deliver congestion information.

## Slide 8: ECN-based Transports
ECN-enabled end-hosts
  React to ECN by adjusting sending rates
ECN-aware switches
  Perform ECN marking based on Active Queue Management (AQM) policies
  Our focus
Notes: In this work, we focus on the ECN marking scheme on the switch.

## Slide 9: ECN-aware Switches
Adopt RED to perform ECN marking
  RED = Random Early Detection
Notes: Today’s commodity switches typically adopt RED, random early detection, to perform ECN marking.

## Slide 10: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
  Track buffer occupancy of different egress entities
Notes: More specially, there are several ECN/RED implementation on the switch, such as per-queue, per-port and per-service-pool ECN/RED. The key difference among these schemes is that they track buffer occupancy of different egress entities to make ECN marking decisions.

## Slide 11: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
port
queue 1
queue 2
Notes: In per-queue ECN marking, we track the buffer occupancy of each queue to make ECN marking decisions. Each queue has its own ECN marking threshold and performs ECN marking independently to other queues. An arrival packet gets ECN marked if the per-queue buffer occupancy is larger than per-queue ECN marking threshold.

## Slide 12: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
port
queue 1
queue 2
Notes: In per-port ECN marking, we track the total buffer occupancy of a switch port to make ECN marking decisions. Each port has its own ECN marking threshold. An arrival packet gets ECN marked if the per-port buffer occupancy is larger than the per-port ECN marking threshold.

## Slide 13: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
port
queue 1
queue 2
port
queue 3
queue 4
shared buffer
Notes: In per-service-pool ECN marking, we track the total buffer occupancy of a shared buffer region to make ECN marking decisions.

## Slide 14: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
Leverage multiple queues to classify traffic
  Isolate traffic from different services/applications
Notes: As we have shown, commodity switches have provided multiple queues for each egress port. Current operation practice is to leverage multiple queues to isolate traffic from different services/applications.

## Slide 15: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
Leverage multiple queues to classify traffic
  Isolate traffic from different services/applications
Services running DCTCP
Services running TCP
Services running UDP
Notes: For example, we can isolate traffic from different services based on their protocols.

## Slide 16: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
Leverage multiple queues to classify traffic
  Isolate traffic from different services/applications
Real-time services
Best-effort services
Background services
Notes: We can also isolate services based on their importance.

## Slide 17: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
Leverage multiple queues to classify traffic
  Isolate traffic from different services/applications
  Weighted max-min fair sharing among queues
Real-time services
Best-effort services
Background services
Weight = 4
Weight = 2
Weight = 1
Notes: Among the queues, operators typically enforce weighted max-min fair sharing policy since they don’t want to persistently starve a whole service for long time. For example, we can assign a high weight to more important real-time services and a low weight to less important background services.

## Slide 18: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
Leverage multiple queues to classify traffic
  Isolate traffic from different services/applications
  Weighted max-min fair sharing among queues
  Perform ECN marking in multi-queue context
Notes: In summary, in production data centers with multiple services, we need to perform ECN marking in multi-queue context. This is the problem we want to explore.

## Slide 19: ECN marking with Single Queue
Notes: To understand this problem, we start from the simplest scenario, ECN marking with single queue.

## Slide 20: ECN marking with Single Queue
RED Algorithm
Notes: This figure shows that how RED calculates marking probability based on buffer occupancy. It has at least three parameters: Kmin, Kmax and Pamx.

## Slide 21: ECN marking with Single Queue
RED Algorithm
Practical Configuration
(e.g., DCTCP)
Notes: In practice, operators typically set Kmin and Kmax to the same value. In this way, there is only one ECN marking threshold, K, that we need to configure. A packet gets marked if the buffer occupancy is larger than K.

## Slide 22: ECN marking with Single Queue
To achieve 100% throughput
Notes: To achieve 100% throughput for synchronized TCP flows, K should be no smaller than C times RTT times lambda.

## Slide 23: ECN marking with Single Queue
To achieve 100% throughput
Determined by congestion control algorithms
Notes: C times RTT is bandwidth delay product. Lambda is a fixed parameter determined by congestion control algorithms at end hosts. For example, lambda is 1 for regular ECN-enabled TCP which simply cuts window by half in the presence of ECN.

## Slide 24: ECN marking with Single Queue
To achieve 100% throughput
Standard ECN marking threshold
Notes: Here, we call C times RTT times lambda as the standard ECN marking threshold since it is the value we can use to fully utilize link capacity while delivering low latency.

## Slide 25: ECN marking with Single Queue
To achieve 100% throughput
The standard threshold is relatively stable in DCN,
e.g., 65 packets for 10G network (DCTCP paper)
Notes: In homogeneous data center networks, RTT is relatively stable. And C is given, lambda is given. So it is feasible for us to compute a static value as the standard ECN marking threshold. For example, in DCTCP paper, the authors recommend using 65 packets as the marking threshold for 10G network.

## Slide 26: ECN marking with Multi-Queue (1)
Notes: Now, we move to ECN marking in multi-queue context.

## Slide 27: ECN marking with Multi-Queue (1)
Per-queue with the standard threshold
standard threshold
port
queue 1
queue 2
queue 3
Don’t mark
Mark
Notes: In multi-queue context, per-queue ECN making is widely employed by operators due to its good isolation among different queues. To fully utilize the link capacity in any condition, many operators configure the standard ECN marking threshold for each queue. In this way, any queue can independently fully utilize the link capacity regardless of traffic dynamics. To the best of our knowledge, this is current operation practice in industry.

## Slide 28: ECN marking with Multi-Queue (1)
Per-queue with the standard threshold
  Increase packet latency
standard threshold
port
queue 1
queue 2
queue 3
Don’t mark
Mark
Notes: However, such configuration will increase packet latency when many queues are concurrently active.

## Slide 29: ECN marking with Multi-Queue (1)
Per-queue with the standard threshold
  Increase packet latency
Evenly classify 8 long-lived flows into a varying number of queues
Notes: To confirm this, we even classify 8 long-lived flows into a varying number of queues. As we can see from this figure, more queues lead to worse latency.

## Slide 30: ECN marking with Multi-Queue (2)
Per-queue with the minimum threshold
Normalized weight
minimum threshold
port
queue 1
queue 2
queue 3
Don’t mark
Mark
Notes: Realizing above limitation, an alternative approach is to divide the standard ECN marking threshold into different queues based on queue weights. In this formula, Wi is the weight of queue i. So Wi over the sum of Wj is the normalized weight of queue i. Such configuration can achieve good latency even when all the queues are concurrently active.

## Slide 31: ECN marking with Multi-Queue (2)
Per-queue with the minimum threshold
  Degrade throughput
minimum threshold
port
queue 1
queue 2
queue 3
Don’t mark
Mark
Notes: However, it will degrade throughput when very few queues are active simultaneously.

## Slide 32: ECN marking with Multi-Queue (2)
Per-queue with the minimum threshold
  Degrade throughput
Overall Average FCT
Average FCT (>10MB)
Notes: To confirm this, we consider an extreme case where only one queue is active. As we can see from these figures, the threshold of 16 packets can achieve better performance compared to the threshold of 2 packets.

## Slide 33: ECN marking with Multi-Queue (3)
Per-port
standard threshold
port
queue 1
queue 2
queue 3
Don’t mark
Mark
Notes: Unlike previous two per-queue-based approaches, we can use per-port ECN/RED to achieve both high throughput and low latency by setting the per-port marking threshold to the standard ECN marking threshold.

## Slide 34: ECN marking with Multi-Queue (3)
Per-port
  Violate weighted fair sharing
standard threshold
port
queue 1
queue 2
queue 3
Don’t mark
Mark
Notes: However, per-port ECN/RED cannot ensure isolation among different queues. Packets from one queue can get ECN marked due to the buffer occupancy of other queues. As a result, per-port ECN/RED can seriously violate the weighted fair sharing policy among queues. We believe this problem will be more serious if we use per-service-pool ECN/RED as queues from different ports can interfere with each other.

## Slide 35: ECN marking with Multi-Queue (3)
Per-port
  Violate weighted fair sharing
Both services have a equal-weight dedicated queue on the switch
Notes: To confirm this impairment, we classify traffic into two services. Both services have a equal-weight dedicated queue on the switch. According to scheduling policy, both services should always fairly share the link capacity. However, as we can see, with per-port ECN/RED, service 2 can get more bandwidth when we increase its number of flows.

## Slide 36: Question
Can we design an ECN marking scheme with following properties:
  Deliver low latency
  Achieve high throughput
  Preserve weighted fair sharing
  Compatible with legacy ECN/RED implementation
Notes: Here, we take one step back and ask a question, can we design an ECN marking scheme that achieve low latency and high throughput while strictly preserving weighted fair sharing policy? In addition, for hardware implementation friendliness, we also require the scheme should perform RED like enqueue ECN marking. More specially, our solution should compare buffer occupancy against a threshold at the enqueue side to make marking decisions.

## Slide 37: Question
Can we design an ECN marking scheme with following properties:
  Deliver low latency
  Achieve high throughput
  Preserve weighted fair sharing
  Compatible with legacy ECN/RED implementation
Our answer: MQ-ECN
Notes: Our answer is MQ-ECN

## Slide 38
MQ-ECN’S DESIGN
Notes: Now, let’s move to the design of MQ-ECN

## Slide 39: Start from GPS Model
queues share the link with capacity
2
.
.
.
N
1
Generalized Processor Sharing (GPS)
Notes: We start from ideal GPS model. Consider we have N queues share the link with capacity C. The underlying scheduler is generalized processor sharing (GPS).

## Slide 40: Start from GPS Model
queues share the link with capacity
2
.
.
.
N
1
Input Rate
.
.
.
Notes: The input rate of queue i is Ri.

## Slide 41: Start from GPS Model
queues share the link with capacity
2
.
.
.
Weight
N
1
Input Rate
.
.
.
.
.
.
Notes: The weight of queue i is Wi.

## Slide 42: Start from GPS Model
queues share the link with capacity
2
.
.
.
Weight
N
1
Input Rate
.
.
.
.
.
.
Output Rate
.
.
.
Weighted Fair Share Rate
Notes: When the link is congested, according to weighted max-min fairness, we have the following equation. Alpha is unique solution for the equation. Wi times alpha is also called weighted fair share rate. The output rate of queue i is the minimum value between input rate Ri and weighted fair share rate Wi alpha.

## Slide 43: Start from GPS Model
queues share the link with capacity
Use ECN to throttle queue i if
2
.
.
.
Weight
N
1
Input Rate
.
.
.
.
.
.
Output Rate
.
.
.
Notes: When input rate Ri is larger than weighted fair share rate Wi alpha, queue i is congested. For such kind of queues, we should use ECN to throttle them.

## Slide 44: Start from GPS Model
queues share the link with capacity
2
.
.
.
Weight
N
1
Input Rate
.
.
.
.
.
.
Output Rate
.
.
.
Notes: To throttle queue i, we should set the marking threshold of queue i to Wi alpha times RTT times lambda. So the challenge is how can we derive Wi alpha in highly dynamic data center networks.

## Slide 45: Start from GPS Model
queues share the link with capacity
2
.
.
.
Weight
N
1
Input Rate
.
.
.
.
.
.
Output Rate
.
.
.
bit-by-bit round robin
Notes: We leverage the special properties of GPS scheduler to solve it. Note that GPS scheduler performs bit by bit round robin scheduling.

## Slide 46: Start from GPS Model
queues share the link with capacity
2
.
.
.
Quantum
N
1
bits
bits
bits
Input Rate
.
.
.
.
.
.
Output Rate
.
.
.
bit-by-bit round robin
Notes: In each round, queue i can transmit Wi bits at most.

## Slide 47: Start from GPS Model
queues share the link with capacity
2
.
.
.
Quantum
N
1
Input Rate
.
.
.
.
.
.
Output Rate
.
.
.
Time of a round:
Notes: We use quantum i to denote Wi bits. The time of a round is denoted as T round, which can be measured directly. A congested queue is likely to use up its quantum in a round.

## Slide 48: Start from GPS Model
queues share the link with capacity
2
.
.
.
N
1
Input Rate
.
.
.
Output Rate
.
.
.
Time of a round:
Quantum
.
.
.
Notes: Therefore, we can use quantum i over T round to estimate weighted fair share rate.

## Slide 49: MQ-ECN
queues share the link with capacity
Notes: So the marking threshold of queue i can be given as quantum i over T round times RTT times lambda. This is how MQ-ECN calculates per-queue ECN marking thresholds.

## Slide 50: MQ-ECN
Why does it work?
Notes: So you may wonder why this works? Why this formula can achieve all of our design goals.

## Slide 51: MQ-ECN
  Deliver low latency
  Achieve high throughput
  adapts to traffic dynamics
Notes: First of all, we find that, T round reflects traffic dynamics. When many queues are active, T round becomes very large. MQ-ECN reduces per-queue marking thresholds to achieve low latency. When few queues are active, T round is small. MQ-ECN increases per-queue thresholds to achieve high throughput.

## Slide 52: MQ-ECN
  Deliver low latency
  Achieve high throughput
  Preserve weighted fair sharing
  is in proportion to the weight
Notes: Second, quantum i ensures that marking thresholds of different queues are in proportional to their weights. Therefore, MQ-ECN can strictly preserve weighted fair sharing policy.

## Slide 53: MQ-ECN
  Deliver low latency
  Achieve high throughput
  Preserve weighted fair sharing
  Compatible with legacy ECN/RED implementation
  Per-queue ECN/RED with dynamic thresholds
Notes: Third, in this formula, quantum i, RTT and lambda are all given. T round is varying according to traffic dynamics. So, MQ-ECN is essentially a per-queue ECN/RED scheme with dynamic thresholds.

## Slide 54: MQ-ECN
  Deliver low latency
  Achieve high throughput
  Preserve weighted fair sharing
  Compatible with legacy ECN/RED implementation
More details
  Handle inaccurate estimation of
  Apply to round-robin packet schedulers
    DWRR, WRR, etc.
Notes: In the paper, we also discuss how to handle inaccurate estimation of T round and how to apply the formula to round-robin packet schedulers which are widely implemented in switching chips to approximate GPS. For these details, please refer to our paper.

## Slide 55: Testbed Evaluation
MQ-ECN software prototype
  Linux qdisc kernel module performing DWRR
Testbed setup
  9 servers are connected to a server-emulated switch with 9 NICs
  End-hosts use DCTCP as the transport protocol
Benchmark traffic
  Web search (DCTCP paper)
More results in large-scale simulations
Notes: We have implemented a MQ-ECN software prototype as a Linux qdisc kernel module. We build a testbed with 9 servers connected to a server-emulated software switch. At end-host, we use DCTCP as the transport protocol. We generate realistic traffic according to the web search workload in DCTCP paper. We also conduct large-scale simulations to complement our testbed experiments. Here, we just show testbed experiment results.

## Slide 56: Static Flow Experiment
Service 1
Service 2
weight
1
1 flow
4 flows
1
Notes: We start from a simple static flow experiment. In this experiment, service 1 has 1 flow while service 2 has 4 flows. Both services have a equal-weight queue on the switch.

## Slide 57: Static Flow Experiment
Notes: This figure gives aggregate goodputs of two services achieved by MQ-ECN. In contrast to results achieved by per-port ECN/RED, both services fairly share the link capacity regardless of the number of flows.

## Slide 58: Static Flow Experiment
  MQ-ECN preserves weighted fair sharing
Notes: This indicates that MQ-ECN can strictly preserve weighted fair sharing policy.

## Slide 59: Realistic Traffic: Small Flows (<100KB)
Balanced traffic pattern
Unbalanced traffic pattern
Notes: These figures show FCT results of small flows in realistic traffic workload. MQ-ECN achieves comparable performance as the minimum threshold while greatly outperforming the standard threshold. Compared to per-queue ECN/RED with the standard threshold, MQ-ECN can achieve up to 60% and 40% lower average FCT for small flows, respectively.

## Slide 60: Realistic Traffic: Small Flows (<100KB)
  MQ-ECN achieves low latency
Balanced traffic pattern
Unbalanced traffic pattern
Notes: This indicates that MQ-ECN can achieve low latency.

## Slide 61: Realistic Traffic: Large Flows (>10MB)
Balanced traffic pattern
Unbalanced traffic pattern
Notes: These figures gives the results of large flows. As we can see, MQ-ECN performs very similar as the standard threshold while obviously outperforming the minimum threshold.

## Slide 62: Realistic Traffic: Large Flows (>10MB)
  MQ-ECN achieves high throughput
Balanced traffic pattern
Unbalanced traffic pattern
Notes: This indicates that MQ-ECN can achieve high throughput.

## Slide 63: Conclusions
Identify performance impairments of existing ECN/RED schemes in multi-queue context
MQ-ECN: simple, yet effective
  High throughput, low latency, weighted fair sharing
  Currently, apply to round-robin packet schedulers
ECN marking scheme for arbitrary schedulers is an important ongoing effort
Code: http://sing.cse.ust.hk/projects/MQ-ECN
Notes: In this work, we identify performance impairments of existing ECN/RED schemes in multi-queue context. Then we propose MQ-ECN, a simple yet effective ECN/RED scheme for round-robin packet schedulers. MQ-ECN can achieve high throughput and low latency while preserving weighted fair sharing policy. In the future, we expect to design a ECN marking scheme for arbitrary packet schedulers. The code and data is available in this website.

## Slide 64: Thanks!

## Slide 65: Support Arbitrary Packet Schedulers
Find a general solution to estimate per-queue effective draining rate
  Draining rate should be measured when the queue keeps congested
  Measurement window is hard to decide