## Slide 1: Empowering Azure Storage with RDMA
Wei Bai
Presenting collective work of many teams in Microsoft
Peking University
Notes: Hello everyone, I am very happy to be here to present collective work of Azure and MSR on RDMA networking

## Slide 2: Project Contributors
  Wei Bai, Shanim Sainul Abdeen, Ankit Agrawal, Krishan Kumar Attre, Paramvir Bahl, Ameya Bhagat, Gowri Bhaskara, Tanya Brokhman, Lei Cao, Ahmad Cheema, Rebecca Chow, Jeff Cohen, Mahmoud Elhaddad, Vivek Ette, Igal Figlin, Daniel Firestone, Mathew George, Ilya German, Lakhmeet Ghai, Eric Green, Albert Greenberg, Manish Gupta, Randy Haagens, Matthew Hendel, Ridwan Howlader, Neetha John, Julia Johnstone, Tom Jolly, Greg Kramer, David Kruse, Ankit Kumar, Erica Lan, Ivan Lee, Avi Levy, Marina Lipshteyn, Xin Liu, Chen Liu, Guohan Lu, Yuemin Lu, Xiakun Lu, Vadim Makhervaks, Ulad Malashanka, David A. Maltz, Ilias Marinos, Rohan Mehta, Sharda Murthi, Anup Namdhari, Aaron Ogus, Jitendra Padhye, Madhav Pandya, Douglas Phillips, Adrian Power, Suraj Puri, Shachar Raindel, Jordan Rhee, Anthony Russo, Maneesh Sah, Ali Sheriff, Chris Sparacino, Ashutosh Srivastava, Weixiang Sun, Nick Swanson, Fuhou Tian, Lukasz Tomczyk, Vamsi Vadlamuri, Alec Wolman, Ying Xie, Joyce Yom, Lihua Yuan, Yanzhao Zhang, Brian Zill, and many others
Technical support from Arista Networks, Broadcom, Cisco, Dell, Keysight, NVIDIA
Notes: This is the agenda of my talk today

## Slide 3: Agenda
Background
RDMA Deployment for Azure Storage
Problems, Lessons and Future Directions
Notes: This is the agenda of my talk today

## Slide 4: Remote Direct Memory Access (RDMA)
Memory
Buffer A
Write local buffer at address A to remote buffer at address B
Buffer B is filled
DMA
Application
Application
Memory
Buffer B
DMA
Requester
Responder
Allocate
Allocate
  RDMA bypasses host OS stack
   frees host CPU, lowers latency
Notes: Let’s start with basic concept of RDMA. I think many of you know DMA, direct memory access. This is a feature that allows certain hardware subsystems to access main memory independently of CPU. RDMA is essentially remote DMA that crosses different machines.
In this example, there are two hosts which are connected by the network. The requester application tells its NIC ‘hey, can you send data I store in local buffer A to a remote buffer B’.
[click]
The requester’s NIC fetches data from host memory using DMA without involvement of CPU, assemble data into packets, and [click] send packets to the destination NIC through the network.
[click]
Then destination NIC de-assemble packets to get data, writes data to the memory B, and tells the responder application “Hey, someone writes something to your buffer B”
[click]
This data exchange process does not involve network stack running in OS kernel, thus freeing CPU cores. Compared to OS network stack, NIC hardware can provide much lower processing latency and better throughput.

## Slide 5: Performance Benefits of RDMA
RDMA single thread ~40Gbps
RDMA CPU ~0%
RDMA latency 1~2 μs
Measurement on Mellanox ConnectX-3 Pro 40Gbps NIC
Credit: Zhu et al. “Congestion Control for Large-Scale RDMA Deployments” in SIGCOMM 2015
Latest RDMA NICs can achieve 200Gbps/400Gbps for a single flow

## Slide 6: RDMA Programming Model
Queue Pair = Send Queue + Receive Queue
Verbs: send, receive, write and read
HCA = Host Channel Adapter = NIC

## Slide 7: RDMA Networking Techniques
InfiniBand (IB)
Widely used in super computers.
Lossless networks
Special hardware which is incompatible with Ethernet/IP
iWARP
Deliver RDMA services over TCP/IP
Vanilla lossy Ethernet
Expensive & Bad performance due to high complexity
RoCE (v2)
RDMA over converged Ethernet
Lossless Ethernet
Cheap & Good performance
Notes: There are mainly three types of RDMA techniques.

## Slide 8: RDMA Networking Techniques
InfiniBand (IB)
Widely used in super computers.
Lossless networks
Special hardware which is incompatible with Ethernet/IP
iWARP
Deliver RDMA services over TCP/IP
Vanilla lossy Ethernet
Expensive & Bad performance due to high complexity
RoCE (v2)
RDMA over converged Ethernet
Lossless Ethernet
Cheap & Good performance
RoCE (v2)
RDMA over converged Ethernet
Lossless Ethernet
Cheap & Good performance
Suitable for datacenter-scale deployments
Notes: There are mainly three types of RDMA techniques.

## Slide 9: RoCE is not resilient to losses like TCP*
Experiment setup:
  The sender keeps transmitting 10KB messages back-to-back over a persistent connection
Tofino Switch
Sender
Receiver
NVIDIA CX4 NIC
NVIDIA CX4 NIC
 | No drop | Drop 1st packet of the message
TCP | 64us | 159us
RDMA | 5.75us | 199us
Message completion times in difference scenarios
*Recent RDMA NICs such as NVIDIA CX5 and CX6 have significantly improved retransmission performance
Notes: However, RDMA is not resilient to losses like TCP. In this experiment, we have two CX4 nodes connected to a Tofino programmable switch. When there is no packet drop, as we can see, RDMA significantly outperforms TCP. But if we program the switch to drop the first packet of every message, RDMA’s performance is even poor than TCP due to very slow retransmission in hardware

## Slide 10: Basic Challenges of RoCE
RoCE assumes a lossless network, but packet loss happens in DCs today and is used by TCP to infer congestion
Option: Use Priority-based Flow Control (PFC), which is supported by Ethernet switches, to eliminate congestion loss
Prio 1
Prio 2
Prio 1
Prio 2
Egress Port
Ingress Port
Data Packet
Pause Frame
XOFF Threshold
Notes: RoCE assumes a lossless network. However, we know that packet loss due to congestion is common in datacenters today and this is used by TCP as the important signal to infer congestion.
[click] To eliminate congestion lossless in datacenters, one option is using priority-based flow control, which is supported by Ethernet switches in our datacenters.
This figure shows how PFC works. There are two priorities each with a XOFF threshold. If the ingress queue length reaches the Xoff threshold, the switch sends red pause frame to the upstream device to tell it to stop sending data.

## Slide 11: Problems of PFC
Head-of-line (HOL) blocking
Switch
Port 1
Port 2
Port 3
Port 4
Data packets
Flow1: port 1 -> port 4
Flow2: port 2 -> port 4
Flow3: port 1 -> port 3
Flow 3
Flow 1
Flow 2

## Slide 12: Problems of PFC
Head-of-line (HOL) blocking
Switch
Port 1
Port 2
Port 3
Port 4
Flow1: port 1 -> port 4
Flow2: port 2 -> port 4
Flow3: port 1 -> port 3
Data packets
PFC
The switch sends PFC pause frames from port 1 and 2
Flow 3
Flow 1
Flow 2

## Slide 13: Problems of PFC
Head-of-line (HOL) blocking
Switch
Port 1
Port 2
Port 3
Port 4
Flow1: port 1 -> port 4
Flow2: port 2 -> port 4
Flow3: port 1 -> port 3
Data packets
PFC
Flow 3 is paused though it does not create any congestion!
The switch sends PFC pause frames from port 1 and 2
Flow 3
Flow 1
Flow 2

## Slide 14: Problems of PFC
Head-of-line (HOL) blocking
Mad NICs and switches send PFC frames when there is no congestion
Credit: Chuanxiong Guo “RDMA in Data Centers: Looking Back and Looking Forward” in APNet 2017

## Slide 15: Problems of PFC
Head-of-line (HOL) blocking
Mad NICs and switches send PFC frames when there is no congestion
Credit: Chuanxiong Guo “RDMA in Data Centers: Looking Back and Looking Forward” in APNet 2017
PFC can spread congestion, is unfair, and
can lead to deadlocks!
Zhu et al. [SIGCOMM’15], Guo et al. [SIGCOMM’16], Hu et al. [HotNets’17]

## Slide 16: Agenda
Background
RDMA Deployment for Azure Storage
Problems, Lessons and Future Directions
Notes: This is the agenda of my talk today

## Slide 17: Disaggregated Storage in Azure
Azure Storage
Azure Compute

## Slide 18: Disaggregated Storage in Azure
Azure Storage
Azure Compute
Frontend
Backend

## Slide 19: Disaggregated Storage in Azure
Host Domain
VM1
Compute Server
VM2
Extent Node
Primary
Secondary
Secondary
Extent Node
Extent Node
Partition Server
Frontend
Storage
Disk Write Request
Disk Write Response

## Slide 20: Disaggregated Storage in Azure
Azure Storage
Azure Compute
Frontend
Backend
RDMA

## Slide 21: RDMA Benefits benefits
For Azure
Sell freed-up CPU cores in compute
For Customers
Buy cheaper servers in storage
Lower IO latency and jitter
Core savings

## Slide 22
RDMA
TCP
Credit: Jitu Padhye
Notes: This is a good analogy for TCP and RDMA. TCP is as slow as my Honda CRV and RDMA is like F1 race car.

## Slide 23: Network Architecture of an Azure Region
Server
T0
T1
T2
Regional Hub
Data Center
Cluster
Notes: This figure gives the topology of an Azure region. Green ones are servers. Then there are four tiers of switches, T0, T1, T2 and RH.

## Slide 24: Azure needs intra-region RDMA
Server
T0
T1
T2
Regional Hub
Compute
Compute
Storage
Storage
RDMA
Notes: In Azure, a compute VM can fetch the blob from any storage cluster inside the region. Therefore, RDMA traffic may cross different datacenters.

## Slide 25: Large and variable latency end-to-end
Server
T0
T1
T2
Regional Hub
5m
40m
300m
Up to 100km
Intra-rack RTT: 2us
Intra-DC RTT: 10s of us
Intra-region RTT: 2ms
500us delay
Notes: This means our RDMA traffic will experience a large RTT variation due to long haul cables between T2 and RH.

## Slide 26: Heterogenous NICs
Server
T0
T1
T2
Regional Hub
Gen1
Gen1
Gen2
Gen3
Different types of NICs have different transport (e.g., DCQCN) implementations
Notes: We also need to handle heterogenous NIC hardware.
[click]
In Azure, different clusters use different hardware. Old clusters use CX3 while the new ones use CX4 and CX5. And they have different DCQCN implementations.

## Slide 27: Heterogenous Switches
Server
T0
T1
T2
Regional Hub
Single-ASIC Shallow-buffered Pizza Box Switches
Multi-ASIC Deep-buffered Chassis Switches
Notes: In addition to NIC, our switches are also heterogenous. At the high level, we can classify our data center switches into two categories. [click] At T0 and T1, ,[click] At T2 and RH

## Slide 28: Heterogenous Switches
Server
T0
T1
T2
Regional Hub
Single-ASIC Shallow-buffered Pizza Box Switches
Multi-ASIC Deep-buffered Chassis Switches
Many vendors
Notes: And all the cloud providers want to avoid vendor lock-in problem. So we use switches from different vendors.

## Slide 29: Our Solutions in 1 Slide
RDMA-based protocols: sU-RDMA and sK-RDMA
Host monitoring: RDMA Estats
Unified switch software: SONiC
Congestion control: DCQCN + PFC

## Slide 30: sU-RDMA* for Storage Backend
Translate Socket APIs to RDMA verbs
  Three transfer modes based on message sizes
TCP and RDMA transitions
  If the NIC becomes “mad”, we should switch to TCP
  After some time, we should try recovering back to RDMA.
Chunking: static window
*sU-RDMA = storage user space RDMA

## Slide 31: sK-RDMA* for Storage Frontend
*sK-RDMA = storage kernel space RDMA
Extend SMB Direct. Run RDMA in kernel space.
According to IB spec, the NIC should wait for the completion of the FMR before processing any subsequently posted requests

## Slide 32: sK-RDMA* for Storage Frontend
*sK-RDMA = storage kernel space RDMA
Extend SMB Direct. Run RDMA in kernel space.
Read from any EN

## Slide 33: RDMA Estats
T6 - T1: client latency
T5 - T1: hardware latency
Provide fine-grained latency breakdown for each RDMA operation

## Slide 34: Traditional Switch Ecosystem
ASIC Vendor
Notes: A switch essentially consists of ASIC and switch OS software, which controls the ASIC.
Representative switch ASIC vendors include ..

## Slide 35: Traditional Switch Ecosystem
Switch Vendor
Arista EOS
Cisco IOS
Proprietary Switch OS
Switch Box
ASIC Vendor
Notes: Switch vendors buy ASICs, build the switch OS to control ASICs. These switch OSs are not open sourced. And most importantly, the switch Oses are typically very complex because they includes the union of all features requested by all customers over the lifetime of the product.

## Slide 36: Traditional Switch Ecosystem
Cloud Provider
Switch Vendor
ASIC Vendor
Notes: To avoid vendor lock-in problem, cloud providers adopt switches from multiple vendors

## Slide 37: Traditional Switch Ecosystem
ASIC Vendor
Switch Vendor
Low Visibility
Cloud Provider

## Slide 38: SONiC: Software for Open Networking in the Cloud
ASIC Vendor
More apps
SNMP
BGP
DHCP
IPv6
SYNCD
LLDP
RedisDB
TeamD
Utility
Platform
SWSS
Database
BGP
New
New
A Containerized Cross-platform Switch OS
Notes: SONiC stands for ..
SAI provides unified interfaces and behavior models for the switch. ASIC vendors provide implementations of SAI. SAI enables switch OS to use a universal language to talk to different vendors.
SONiC is built on the top of SAI.

## Slide 39: SONiC: Software for Open Networking in the Cloud
ASIC Vendor
More apps
SNMP
BGP
DHCP
IPv6
SYNCD
LLDP
RedisDB
TeamD
Utility
Platform
SWSS
Database
BGP
New
New
A Containerized Cross-platform Switch OS
Cloud Provider
using SONiC
Open Software
+
Standardized Hardware Interfaces
Notes: SONiC stands for ..
SAI provides unified interfaces and behavior models for the switch. ASIC vendors provide implementations of SAI. SAI enables switch OS to use a universal language to talk to different vendors.
SONiC is built on the top of SAI.

## Slide 40: RDMA Features in SONiC
ECN
Shared buffer
PFC
PFC headroom pool
PFC watchdog
Various counters
A SONiC Buffer Template Example
Notes: When we design SONiC, we take RDMA required features into consideration from the day one.
But given these features, how to test them? How to ensure they work as expected?

## Slide 41: RDMA Features in SONiC
ECN
Shared buffer
PFC
PFC headroom pool
PFC watchdog
Various counters
A SONiC Buffer Template Example
If a queue has been in paused state for very long time, drop all its packets
Notes: When we design SONiC, we take RDMA required features into consideration from the day one.
But given these features, how to test them? How to ensure they work as expected?

## Slide 42: How to test RDMA features of SONiC
Software-based tests (single step debugging)
  Block the transmission of a switch port
  Inject a series of packets destined for the blocked port and capture snapshots of switch states accordingly
  Release the port and dump packets
If queue length == 1

## Slide 43: How to test RDMA features of SONiC
Software-based tests (single step debugging)
  Block the transmission of a switch port
  Inject a series of packets destined for the blocked port and capture snapshots of switch states accordingly
  Release the port and dump packets
If queue length == 2

## Slide 44: How to test RDMA features of SONiC
Software-based tests (single step debugging)
  Block the transmission of a switch port
  Inject a series of packets destined for the blocked port and capture snapshots of switch states accordingly
  Release the port and dump packets
If queue length == 3

## Slide 45: How to test RDMA features of SONiC
Software-based tests (single step debugging)
  Block the transmission of a switch port
  Inject a series of packets destined for the blocked port and capture snapshots of switch states accordingly
  Release the port and dump packets
If queue length == 4 and
ECN counter == 1
ECN marking

## Slide 46: How to test RDMA features of SONiC
Software-based tests (single step debugging)
  Block the transmission of a switch port
  Inject a series of packets destined for the blocked port and capture snapshots of switch states accordingly
  Release the port and dump packets
Features covered: buffer model, watermark, scheduling, etc.
  Limitation: cannot test performance-sensitive features

## Slide 47: How to test performance-sensitive features
Control traffic generation at μs and ns timescales
High-resolution measurement of data plane behaviors
Our solution: programmable test hardware from Keysight

## Slide 48: DCQCN uses Explicit Congestion Notification (ECN) as early-warning
DCQCN is a rate-based congestion control algorithm implemented in NIC
Sender
Receiver
Congestion Notifications
Congestion
Marked Packets
Sender lowers rate when notified of congestion and increases o/w
We use both DCQCN and PFC:
  DCQCN reduces how often PFC is triggered.
  PFC is still used as the last resort.
Notes: Given these observations, together with Azure networking and Mellanox, we design DCQCN, a rate-based congestion control algorithm implemented in the NIC. Instead of sensing congestion through packet losses, DCQCN uses explicit congestion notification supported by commodity Ethernet switches to detection congestion and avoid packet losses as much as possible.
[click]
This example shows how DCQCN works. When there is congestion, there must be some queue build-ups in the switch buffer. [click] Let’s assume the marking threshold is 3. So the fourth packet in the buffer will be marked. [click] When the receiver sees this marked packet, it will know that there is congestion in the network and send a special kind of packets, called congestion notification packets, to tell the sender.
[click]
The sender lowers rate when it receives congestion notification packets. Otherwise, it will increase the sending rate.
[click]
We use both DCQCN and PFC in our deployments. We rely on DCQCN to eliminate packet losses in common cases and use PFC as the last resort to handle extreme cases.

## Slide 49: DCQCN + PFC in Production
Different DCQCN implementations on NIC Gen1/2/3
  Gen1 has DCQCN implemented in firmware (slow) and uses a different congestion notification mechanism.
  Solution: modify firmware of Gen2 and Gen3 to make them behave like Gen1
Careful DCQCN tuning for a wide range of RTTs
  Interesting observation: DCQCN has near-perfect RTT fairness
Careful buffer tuning for various switches
  Reserve enough PFC headroom, especially for long cables
  Ensure that ECN kicks in before PFC

## Slide 50: Deployment Practice
Lab Testbed
Test each individual component
DCQCN tuning
Test Clusters
End-to-end stress tests (high load, error injection, different servicing flows)
Finalize DCQDN parameters
Production Clusters
Minimize the impact of servicing switches and NICs to customer traffic

## Slide 51: 100x100 100 Gbps over 100 km
O(1018) bytes / day, O(109) IOs / day
~70% of bytes. TCP distant second.
Significant perf improvements and COGS savings
Possibly largest RDMA deployment in the world

## Slide 52: Agenda
Background
RDMA Deployment for Azure Storage
Problems, Lessons and Future Directions
Notes: This is the agenda of my talk today

## Slide 53: Case Study: a DCQCN implementation bug
Gen1 (40G)
Gen2 (50G)
Notes: This is part of our testbed.
[click]
We use a dumbbell topology with two racks of servers to run all to all workloads.

## Slide 54: Discovering the problem
8 Hosts: 4 with Gen1 NIC (40Gbps), 4 with Gen2 NIC (50 Gbps)
All-to-all traffic pattern, 10 QPs per host pair, RDMA Write
Aggregate goodput: 200.6Gbps
Gen1: 34Gbps goodput
Gen2: 17Gbps goodput
Gen1: 34Gbps goodput
Gen2: 17Gbps goodput

## Slide 55: Analysis
Max-min fairness to predict throughput in MSR cluster
  All hosts should be sending & receiving at line rate
  Expected aggregate throughput per host-pair
    Gen1 to Gen1: 10Gbps
    Gen1 to Gen2: 2.5Gbps
    Gen2 to Gen1: 2.5Gbps
    Gen2 to Gen2: 13.3Gbps
Notes: So what is the problem here? We use our domain knowledge to analyze this problem. We know that DCQCN should be able to achieve max-min fairness in such scenarios. So we use water-filling algorithm to derive the expected throughput for each host pair.

## Slide 56: Analysis
Max-min fairness to predict throughput in MSR cluster
  All hosts should be sending & receiving at line rate
  Expected aggregate throughput per host-pair
    Gen1 to Gen1: 10Gbps
    Gen1 to Gen2: 2.5Gbps
    Gen2 to Gen1: 2.5Gbps
    Gen2 to Gen2: 13.3Gbps 2.5Gbps
Finding: Gen2’s sending rate is limited by rate of the slowest receiver
The vendor found a HoL blocking firmware bug in Gen2 NIC.

## Slide 57: After deploying the fix
Same configuration as before
Gen1: 34Gbps goodput
Gen2: 48Gbps goodput
Gen1: 34Gbps goodput
Gen2: 48Gbps goodput
Aggregate goodput improved from 200Gbps to 316Gbps
Notes: After deploying the fix, our experiment results match theory analysis.

## Slide 58: Other Problems Found
PFC and MACsec
  Different switches have no agreement on whether PFC frames sent should be encrypted or what to do with arriving encrypted PFC frames
Slow receiver due to loopback RDMA traffic
  Loopback RDMA traffic and inter-host RDMA traffic cause host congestion
Fast Memory Registration (FMR) hidden fence
  In sK-RDMA, the send queue consists of many FMR/Send pairs
  The NIC processes the FMR request only after the completions of previously posted requests

## Slide 59: Lessons and Open Problems
Failovers are very expensive for RDMA
Host network and physical network should be converged
Switch buffer is increasingly important and needs more innovations
Cloud needs unified behavior models and interfaces for network devices
Testing new network devices is critical and challenging

## Slide 60: Lessons and Open Problems
Failovers are very expensive for RDMA
Host network and physical network should be converged
Switch buffer is increasingly important and needs more innovations
Cloud needs unified behavior models and interfaces for network devices
Testing new network devices is critical and challenging

## Slide 61: Lessons and Open Problems
Failovers are very expensive for RDMA
Host network and physical network should be converged
Switch buffer is increasingly important and needs more innovations
Cloud needs unified behavior models and interfaces for network devices
Testing new network devices is critical and challenging

## Slide 62: Lessons and Open Problems
Failovers are very expensive for RDMA
Host network and physical network should be converged
Switch buffer is increasingly important and needs more innovations
Cloud needs unified behavior models and interfaces for network devices
Testing new network devices is critical and challenging

## Slide 63: Lessons and Open Problems
Failovers are very expensive for RDMA
Host network and physical network should be converged
Switch buffer is increasingly important and needs more innovations
Cloud needs unified behavior models and interfaces for network devices
Testing new network devices is critical and challenging

## Slide 64: Thank You!